## Slide 1: P4 demo: a basic L2/L3 switch in 170 LOC
Mihai Budiu
netdev0.1
Ottawa, February 15, 2015

## Slide 2: Setup
Mininet
Router control
Tables
P4 program
P4 compiler
P4 software switch
Data plane
Table access API
RPC
h1
h2
Notes: ﻿cd p4factory/targets/simple_router
make behavioral
cd ../../..
﻿cd mininet-demo
sudo python 1sw_demo.py --behavioral-exe ../p4factory/targets/simple_router/behavioral-model

## Slide 3: DEMO PART 1
Creating a basic ethernet+IPv4 switch from a P4 program
Tables
P4 program
P4 compiler
P4 software switch
Data plane
P4 compiler

## Slide 4: Layer 3 packet forwarding
IPv4.dst ->
nextHop.ipv4address,
outputPort,
ipv4.ttl
Packet
nextHop.ipv4address ->
ethernet.dst_addr
outputPort ->
ethernet.src_addr
Packet
Control plane
Notes: ﻿mininet> h1 wireshark &
mininet> h1 ping h2 # this should fail
$ ﻿./simple_router_control --thrift-path ../p4factory/targets/simple_router/of-tests/pd_thrift < commands.txt
mininet> h1 ping h2 # this should succeed

## Slide 5: Headers
header_type ethernet_t { fields { dstAddr: 48; srcAddr: 48; etherType: 16; } }
header_type ipv4_t { … }
// no options

## Slide 6: Parser
﻿parser parse_ethernet { extract(ethernet); return select(latest.etherType) { 0x0800 : parse_ipv4; default: ingress; }}
…
parser parse_ipv4 { … } calculated_field ipv4.hdrChecksum { verify ipv4_checksum; update ipv4_checksum; }

## Slide 7: Last table
action rewrite_mac(smac) { modify_field(ethernet.srcAddr, smac); }
table send_frame { reads { std_metadata.egress_port: exact; } actions { rewrite_mac;
drop;
}
size: 256;
}
outputPort ->
ethernet.src_addr

## Slide 8: Complete pipeline
control ingress { apply(ipv4_match); apply(forward); }
control egress { apply(send_frame); }

## Slide 9
1. Compiled a new switch from P4
2. Started switch running

## Slide 10
1. Running wireshark on h1
2. Ping from h1 to h2 does not work
3. Pings sent but no reply returned

## Slide 11: DEMO PART 2
Populate switch tables to enable forwarding
Router control
Tables
P4 software switch
Data plane
Table access API
RPC

## Slide 12
1. Populated all tables; ping starts running
2. Pings sent and reply received

## Slide 13: DEMO PART 3
Counters in the datapath

## Slide 14: Adding counters to table entries
counter send_frame_bytes { type : bytes; direct : send_frame; }
output_port | Action
counter
Table send_frame

## Slide 15
Reading byte counters while ping is running

## Slide 16: DEMO PART 4
Divert traffic

## Slide 17: Diverting traffic
IPv4.dst ->
nextHop.ipv4address,
outputPort,
ipv4.ttl
nextHop.ipv4address ->
ethernet.dst_addr
outputPort ->
ethernet.src_addr
IPv4.dst ->
IPv4.dst
Divert traffic for specific destinations to another destination
Notes: $ ﻿./simple_router_control --thrift-path ../p4factory/targets/simple_router/of-tests/pd_thrift < divert.txt
Mininet> h1 ping h2 # this should fail, but wireshark shows packet coming back

## Slide 18: Modified pipeline
control ingress { apply(divert); apply(ipv4_match); apply(forward); }
control egress { apply(send_frame); }
Notes: ﻿./simple_router_control --thrift-path ../p4factory/targets/simple_router/of-tests/pd_thrift
SimpleRouter: get_ctr send_frame_bytes 0
<reply>
SimpleRouter: ^D

## Slide 19: Diverting traffic
action replaceIp(ipdest) { modify_field(ipv4.dstAddr, ipdest); }
table divert { reads { ipv4.dstAddr: exact;} actions { replaceIp; nop; } size: 256; }

## Slide 20
1. Inserted table entries to divert packets
2. Pings sent and received by same host

## Slide 21: Availability
All this code will be available as FOSS before March 31, 2015 on http://p4.org