## Slide 1: P4: specifying data planes http://P4.org
Mihai Budiu
netdev0.1
Ottawa, February 15, 2015
Notes: The P4 language is still evolving.

## Slide 2: P4 Language Consortium
“Open for participation by any individual or corporation”
http://p4.org
Language spec v1.0.1
Coming soon (3/2015): FOSS release of a reference P4 implementation

## Slide 3: What do we want to achieve?
Switch
Your own protocols
Standard protocols
Datacenter
Currently most useful if you have your own network playground
Notes: P4 will make it possible to roll out new protocols and features (and remove old protocols too).
Today this is mostly useful within closed networks, e.g. datacenters, but this mechanism will accelerate protocol evolution and it may become applicable to broader ecosystems.

## Slide 4: Benefits
Implement (new) protocols
  VxLAN: 175 lines of code
  NVGRE: 183 lines of code
Low overhead (high speed)
Flexible forwarding policies
Improved signaling, monitoring, and troubleshooting
Change functionality with software upgrades
Use only what you need
Notes: P4 should enable all of these, without sacrificing performance. We want to be able to achieve Tbps switching speeds in programmable switches.

## Slide 5: P4 Scope
Control plane
Data plane
Control traffic
Packets
Table mgmt
Control plane
Data plane
P4 Program
Traditional switch
P4-defined switch
P4 table mgmt
Notes: This is the P4 interface, a new interface between the control-plane and the data plane.
The data plane performs mostly stateless high-speed processing.
The data plane is lean and fast; most of the complexity is still in the control plane. P4 does not address this aspect.

## Slide 6: Q: Which data plane? A: Any data plane!
Control plane
Data plane
Programmable switches
FPGA switches
Programmable NICs
Software switches
You name it…
Notes: P4 should be portable across a large spectrum of switch implementations.

## Slide 7: Data plane programmability
Data plane
P4
P4
P4
Programmable blocks
Fixed function
Notes: P4 expresses the behavior of significant data plane functions. It currently is not rich enough to describe the complete functionality of the data plane.

## Slide 8: How does it work?
Programmable
parser
Packet (byte[])
Headers
eth
vlan
ipv4
Programmable
match-action
units
Metadata
eth
mtag
ipv4
Programmable
reassembly
Packet
Payload
err
bcast
port
Queueing
eth
mtag
ipv4
Headers
Notes: How is packet processing performed in P4?
This is a high-level view.

## Slide 9: P4 language
Programmable
parser
Programmable
match-action
units
Programmable
reassembly
State-machine; bitfield extraction
Table lookup and update; bitfield manipulation; control flow
Bitfield assembly
No: memory (pointers), loops, recursion, floating point
Notes: The P4 language has elements corresponding to the previously-described function blocks: parsing, match/action, and reassembly.

## Slide 10: Parsing = State machines
header_type ethernet_t {
fields {
dstAddr : 48;
srcAddr : 48;
etherType : 16;
}
}
parser parse_ethernet {
extract(ethernet);
return select(latest.etherType) {
0x8100 : parse_vlan;
0x800 : parse_ipv4;
0x86DD : parse_ipv6;
}
}
TCP
New
IPv4
IPv6
VLAN
Eth
Notes: The parser is essentially a state-machine driven by the packet header.
It extracts packet fields into general-purpose registers (“metadata”).

## Slide 11: Match
﻿
table ipv4_lpm
{
reads {
ipv4.dstAddr : lpm;
}
actions {
set_next_hop;
drop;
}
}
dstAddr | action
0.* | drop
10.0.0.* | set_next_hop
224.* | drop
192.168.* | drop
10.0.1.* | set_next_hop
Lookup key
Notes: The Match performs table lookups based on metadata.
The table contents is managed by the control plane.

## Slide 12: Actions
action set_nhop(nhop_ipv4_addr, port)
{
modify_field(metadata.nhop_ipv4_addr, nhop_ipv4_addr);
modify_field(standard_metadata.egress_port, port);
add_to_field(ipv4.ttl, -1);
}
nhop_ipv4_addr | port
10.0.0.10 | 1
10.0.1.10 | 2
dstAddr | action
0.* | drop
10.0.0.* | set_next_hop
224.* | drop
192.168.* | drop
10.0.1.* | set_next_hop
Notes: Actions are code fragments that manipulate metadata. They are driven by information obtained from table look-ups.

## Slide 13: Control-Flow
control ingress
{
apply(port);
if (valid(vlan_tag[0])) {
apply(port_vlan);
}
apply (bridge_domain);
if (valid(mpls_bos)) {
apply(mpls_label);
}
retrieve_tunnel_vni();
if (valid(vxlan) or valid(genv) or valid(nvgre)) {
apply(dest_vtep);
apply(src_vtep);
}
}
M/A
M/A
M/A
M/A
M/A
Notes: P4 supports conditional forward-only control-flow.

## Slide 14: Reassembly
Driven by header types
add_header(ipv6);
remove_header(vlan);

## Slide 15: Table contents management
Control plane
Data plane
Manage tables contents
(Tied to P4 program)
Notes: Table contents is uploaded into the data plane by the control plane.

## Slide 16: P4 Summary
Simple language
  Parsing, bit-field manipulation, table lookup, control flow, packet reassembly
Efficient execution (high speed switching)
Simple cost model
Abstract resources
Portable
Expressive:
  New protocols, forwarding policies, monitoring and instrumentation
Notes: We will release the first version of the language soon.
We are actively working on an improved version which fixed some shortcomings – which we plan to release as well.

## Slide 17
Control plane
Data plane
The P4 Programming- Language Interface
Creating a Programming Language Interface in a place where there wasn’t one.