## Slide 1: P4: specifying data planes http://P4.org
Mihai Budiu
VMware Research Group
Intel – Hillsboro, OR July 10, 2018

## Slide 2: My Background
Ph.D. from CMU (computer architecture, compilers)
Microsoft Research (security, big data, machine learning)
Barefoot Networks (P4 design and implementation)
VMware Research (P4, SDNs, big data)
Note: I am not a networking person

## Slide 3: My involvement with P4
Hired at to work on the design and implementation of P4
In Barefoot led the group that created the first P416 draft document
Started (with Chris Dodd) the C++ reference compiler implementation
Main contributor to the open-source P4 compiler front-end, mid-end and several back-ends
Pushed P416 through standardization process
Currently co-chair of the P4 language design working group

## Slide 4: What I can talk about today
P416 programming language
  Language design
  Language/architecture separation
  Portability vs. extensibility
P416 reference compiler architecture
  How to extend the compiler for a new target
Compiling P4->eBPF
  Compiling to eBPF (packet filters)
  Compiling to XDP (packet switching)
  Comparing P4 and eBPF
These are organized as 3 separate PPTX presentations

## Slide 5: What I don’t plan to cover
P414 (the old version of P4)
Run the P4 tutorials (given at P4 developer days)
Demonstrate P4-related tools (compilers, simulators, IDEs)
The P4 control-plane API (P4Runtime)
The P4 Portable Switch Architecture
Various applications written in P4

## Slide 6
P4 & Programmable networks
  Why should you care?
An introduction to P416
  P4 limitations
Conclusions
Presentation outline

## Slide 7: Networking 101
switches/ routers
Data packets

## Slide 8: Switch Control and Data Planes
Control plane
Data plane
Interfaces
Switch architecture
packets

## Slide 9: Traditional switch architecture
Control plane
Data plane
Table management
Look-up tables (policies)
Switch ASIC
Control-plane CPU

## Slide 10: Software-Defined Networking
Dumb control plane
Data plane
Controller
Policies/signaling

## Slide 11: The P4 world
Programmable data plane
SW: P4
Dumb control plane
Upload program
Policies/signaling

## Slide 12: Not just for switches!
Programmable switches
FPGA switches
Programmable network cards
Software switches
Hypervisor switches
You name it…
Programmable data plane
SW: P4
Control plane

## Slide 13: How is this possible?
Hello
?
Datacenter
Most useful if you have your own network playground

## Slide 14: Data-planes
From now on in this presentation we only talk about the data-plane
We expect that SDN will continue to evolve the control-plane
Control plane
Data plane

## Slide 15: WHY SHOULD YOU CARE?

## Slide 16: P4.org Consortium
Carriers, cloud operators, chip cos, networking, systems, universities, start-ups

## Slide 17: Isn’t Open-Flow Enough?
Chart: Headers
| 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4
Headers | 12 | 15 | 36 | 40 | 41
Open-Flow version
Open-flow has never been enough: it keeps changing to describe new protocols
Very fragmented

## Slide 18: Protocols = programs
VxLAN: 175 lines of P4
  Took 4 years from proposal to wide availability
NVGRE: 183 lines of P4
M. Shahbaz, S. Choi, B. Pfaff, C. Kim, N. Feamster, N. McKeown, J. Rexford, PISCES: A Programmable, Protocol-Independent Software Switch SIGCOMM 2016
40 times reduction in the size of the OvS parser
Much easier to add new protocols
Same performance

## Slide 19: Use only what you need
IETF has issued thousands of RFCs
Switch RAM and CPU is very expensive
Network operators can remove protocols
Simpler troubleshooting

## Slide 20: Network monitoring
measurements
(custom headers)
Monitoring
agent
In-Band Network Telemetry (INT)
Improving Network Monitoring and Management with Programmable Data Planes
By Mukesh Hira & LJ Wobker

## Slide 21: Optimize your network
Push application functionality in the network
High speed
Paxos Made Switch-y
Huynh Tu Dang, Marco Canini, Fernando Pedone, Robert Soulé
CCR April 2016

## Slide 22: Network = software
Use software engineering principles and tools
Upgrade your network at any time
Protocols = intellectual property

## Slide 23: AN INTRODUCTION to P416

## Slide 24: Language evolution
P4: Programming Protocol-Independent Packet Processors
Pat Bosshart, Dan Daly, Glen Gibb, Martin Izzard, Nick McKeown, Jennifer Rexford, Cole Schlesinger, Dan Talayco, Amin Vahdat, George Varghese, David Walker ACM SIGCOMM Computer Communications Review (CCR). Volume 44, Issue #3 (July 2014)
P4 v1.0 spec, reference implementation and tools released in Spring 2015 (mostly by Barefoot Networks), Apache 2 license, http://github.com/p4lang.
P416 spec, draft reference implementation and tools released in December 2016; spec finalized May 2017; v1.1 in June 2018 http://github.com/p4lang/p4-spec

## Slide 25: P4 Community
http://github.com/p4lang
http://p4.org
Free membership!
Mailing lists
Workshops
P4 developer days
Academic papers (SIGCOMM, SOSR)

## Slide 26: P4 working groups
Language design: evolves P4
Control-plane API: defines API between control-plane and P4 program (P4Runtime)
Applications: defines interoperable applications (e.g. In-band Network Telemetry)
Architecture (Portable Switch Architecture): standardizes portable architecture models
Education

## Slide 27: Available Software Tools
Compilers for various back-ends
  Netronome chip, Barefoot chip, eBPF, Xilinx FPGA
  (open-source and proprietary)
Multiple control-plane implementations
  SAI, OpenFlow, P4Runtime
Simulators
Testing tools
Sample P4 programs
IntelliJ plugin IDE, editor modes
Tutorials

## Slide 28: P4 software workflow
P4 program
P4 architecture
model
Data plane
P4 compiler
Tables
Dataplane runtime
Control-plane
target
User-supplied
API
Manufacturer supplied
control
signals
extern objects
API
LOAD
LOAD

## Slide 29: P416
Most recent revision of P4
C-like syntax; strongly typed
  No loops, pointers, recursion, dynamic allocation
Spec: http://github.com/p4lang/p4-spec
Reference compiler implementation (Apache 2 license): http://github.com/p4lang/p4c

## Slide 30: P416 Language Overview
Suitable for L2 & 3
High-level, type, memory-safe (no pointers)
Bounded execution (no loops)
Statically allocated (no malloc, no recursion)
Sub-languages:
  Parsing headers
  Packet header rewriting
  Target architecture description

## Slide 31: P416 data plane model
Data plane
P4
P4
P4
Programmable blocks
Fixed function
Interfaces

## Slide 32: Example packet processing pipeline
Programmable
parser
Packet (byte[])
Headers
eth
vlan
ipv4
Programmable
match-action
units
Metadata
eth
mtag
ipv4
Programmable
reassembly
Packet
Payload
err
bcast
port
Queueing/
switching
eth
mtag
ipv4
Headers
Not programmable

## Slide 33: Language elements
Programmable
parser
Programmable
match-action
units
Programmable
reassembly
State-machine; bitfield extraction
Table lookup; bitfield manipulation; control flow
Bitfield packing
Data-types
Bitstrings, headers, structures, arrays
External libraries
Support for custom accelerators
Target
description
Interfaces of programmable blocks
user
target

## Slide 34: Basic data types
bit<N>, int<N>
  e.g., bit<128>, int<1024>
  int is two’s complement
varbit<13>
  Container up to specified size; dynamic size is shorter
  Only operation is copying
bool
enum, error, match_kind
  error { PacketTooShort, ParseError }
  error.PacketTooShort
Only string constants supported
typedef

## Slide 35: Structures, headers
typedef bit<32> IPv4Address;
header IPv4_h { bit<4> version; bit<4> ihl; bit<8> tos; bit<16> totalLen; bit<16> identification; bit<3> flags; bit<13> fragOffset; bit<8> ttl; bit<8> protocol; bit<16> hdrChecksum; IPv4Address srcAddr; IPv4Address dstAddr; }
// List of all recognized headers struct Parsed_packet { Ethernet_h ethernet; IPv4_h ip; }
header = struct + valid bit

## Slide 36: Other derived types
Array of headers
  H[6] arr;
  Fixed size
Unions of headers
  header_union IP { ipv4 v4header; ipv6 v6header; }
Tuples
  tuple<bit<32>, bit<16>>
set<tuple<bit<32>, bit<16>> - implicit only
No recursive types

## Slide 37: Expression language
Standard arithmetic/logic on arbitrary bitstrings
  But no funky undefined cases like in C
2s complement for signed values
No division/modulo
Bit-slicing, bit concatenation
Integers are not Booleans
No implicit casts

## Slide 38: Extern objects
Model hardware accelerators or…
…behaviors not expressible in P4
extern Register<T> { Register(bit<32> size); T read(in bit<32> index); void write(in bit<32> index, in T value); }
Register<bit<32>>(1024) reg;
Method calls using copy-in, copy-out
Like Java interfaces
constructor
Generic type
instantiation

## Slide 39: Packets = byte streams
extern packet_in {
void extract<T>(out T headerLvalue); void extract<T>(out T varSizeHdr, in bit<32> varFieldSizeBits); T lookahead<T>(); bit<32> length(); void advance(in bit<32> bits); }
extern packet_out { void emit<T>(in T hdr); void emit<T>(in bool condition, in T data); }

## Slide 40: Parsing = State machines
parser Parser(packet_in b, out Parsed_packet p) { state start { b.extract(p.ethernet); transition select(p.ethernet.type) { 0x0800: parse_ipv4; default: reject; } }
state parse_ipv4 { b.extract(p.ip); transition accept; } }
src
IP header
dst
IP payload
type
ethernet header
start
parse_ipv4
reject
accept
Parser states can contain cycles => loops bounded by packet size

## Slide 41: Value Sets
parser p(packet_in pk, out Headers h) { value_set<bit<32>>(4) vs; state start { pk.extract(h); transition select(h.f) { vs: next; default: reject; } … } }
A set of 32-bit values changed dynamically by the control plane.

## Slide 42: Actions
action Set_nhop(IPv4Address ipv4_dest, PortId port) { nextHop = ipv4_dest; outCtrl.outputPort = port; }
Action data; from control plane
~ Objects with a single method.
Straight-line code.
Reside in tables; invoked automatically on table match.
class Set_nhop {
IPv4Address ipv4_dest;
PortId port;
void run() {
nextHop = ipv4_dest; outCtrl.outputPort = port
}
}
Java/C++ equivalent code.

## Slide 43: Tables
dstAddr | action
0.0.0.0 | drop
10.0.0.1 | Set_nhop(10.4.3.4, 4)
224.0.0.2 | drop
192.168.1.100 | drop
10.0.1.10 | Set_nhop(10.4.2.1, 6)
table ipv4_match { key = { headers.ip.dstAddr: exact; } actions = { drop; Set_nhop; } default_action = drop; }
Populated by the control plane
Map<K, Action>

## Slide 44: Table = Match-Action Processing
Key | Action
 | action code & data
Lookup table
headers &
metadata
Lookup
Lookup key
Action
action data
action
code
Execute
Control plane
Default action
hit
Data
headers &
metadata

## Slide 45: Control-Flow
control Pipe(inout Parsed_packet headers, in InControl inCtrl,// input port out OutControl outCtrl) { // output port IPv4Address nextHop; // local variable
action Drop_action() { … }
action Set_nhop(…) { … }
table ipv4_match() { … }
…
apply { // body of the pipeline ipv4_match.apply(); if (outCtrl.outputPort == DROP_PORT) return;
dmac.apply(nextHop); if (outCtrl.outputPort == DROP_PORT) return;
smac.apply(); } }
Ipv4_match
dmac
smac

## Slide 46: Packet Construction
control Deparser(in Parsed_packet p, packet_out b) { apply { b.emit(p.ethernet); b.emit(p.ip); } }
Convert headers back into a byte stream.
Only valid headers are emitted.

## Slide 47: P4 Program structure
#include <core.p4> // core library #include <target.p4> // target description
#include "library.p4" // library functions
#include "user.p4" // user program

## Slide 48: Architecture declaration
struct input_metadata { bit<12> inputPort; }
struct output_metadata { bit<12> outputPort; }
parser Parser<H>(packet_in b, out H headers);
control Pipeline<H>(inout H headers, in input_metadata input, out output_metadata output);
control Deparser<H>(in H headers, packet_out p);
package Switch<H>(Parser<H> p, Pipeline<H> p, Deparser<H> d);
Provided by the target manufacturer
H = user-specified header type
Parser
Pipeline
Deparser
Switch

## Slide 49: Support for custom “accelerators”
extern bit<32> random();
extern Checksum16 { void clear(); // prepare unit for computation void update<T>(in T data); // add data to checksum void remove<T>(in T data); // remove data from checksum bit<16> get(); // get the checksum for data added }
External function
External object with methods. Methods can be invoked like functions.
Some external objects can be accessed from the control-plane.

## Slide 50: Execution model
When a block is invoked (parser, control) it executes to completion on a separate thread
  All local variables are thread-local
  Only inter-thread communication possible through extern objects and functions
Execution triggered by outside event (e.g., packet arrival)
Actions execute atomically
  @atomic annotation

## Slide 51: P4 LIMITATIONS

## Slide 52: Limitations of P416
The core P4 language is very small
  Highly portable among many targets
  But very limited in expressivity
Accelerators can provide additional functionality
  May not be portable between different targets
Standard architectures to ensure portability
  Portable switch architecture (PSA)
  Library of standard accelerators (counters, meters, etc)
  No standard smart NIC architecture exists!

## Slide 53: What is missing
Floating point
Pointers, references
Data structures, recursive data types
Dynamic memory management
Loops, iterators (except the parser state-machine)
Recursion
Threads
=> Constant work/byte of header

## Slide 54: What cannot be done in (pure) P4
Multicast or broadcast
Queueing, scheduling, multiplexing
Payload processing: e.g., encryption
Packet trailers
Persistent state across packets
Communication to control-plane
Inter-packet operations (fragmentation and reassembly)
Packet generation
Timers

## Slide 55: How are these done?
Multicast, broadcast, queueing, scheduling, multiplexing
  By target device, controlled by P4 metadata
Persistent state across packets (e.g. per-flow state)
  External objects: registers, counters, meters
Communication to control-plane
  External objects: learning providers
Packet generation
  Control-plane, or external objects
TCP-style reassembly, trailers:
  Not currently done

## Slide 56: Why use P4?
It is a standardized language: you can specify the data-plane precisely
Expressive: express many packet-forwarding policies
High-level, type-safe: compiler-managed abstract resources
Software: treat network devices like software
Killer app: network monitoring

## Slide 57
Control plane
Data plane
UPLOAD
The P4 Programming- Language Interface
Creating a Programming Language Interface in a place where there wasn’t one.

## Slide 58: References
P4: Programming Protocol-Independent Packet Processors Pat Bosshart, Dan Daly, Glen Gibb, Martin Izzard, Nick McKeown, Jennifer Rexford, Cole Schlesinger, Dan Talayco, Amin Vahdat, George Varghese, David Walker ACM SIGCOMM Computer Communications Review (CCR). Volume 44, Issue #3 (July 2014)
The P4-16 Programming Language Mihai Budiu and Chris Dodd ACM SIGOPS Operating Systems Review, Vol. 51, no 1, August, 2017, pages 5-14
P4-16 open-source compiler source tree: https://github.com/p4lang/p4c
P4-16 language v1.1.0 specification: https://p4.org/p4-spec/docs/P4-16-v1.1.0-draft.pdf
Compiler design full presentation: https://github.com/p4lang/p4c/blob/master/docs/compiler-design.pptx
P4Runtime draft spec: https://p4lang.github.io/p4-spec/docs/P4Runtime-v1.0.0.pdf

## Slide 59: Backup slides

## Slide 60: P416 goals
Strictly more expressive than P414
Minimally change and simplify P414
  Same building-blocks: headers, parsers, match-action, control
Well-defined semantics for all constructs
Move target-specific constructs from language into libraries
Support a variety of targets (ASICs, NICs, FPGAs, etc.)
Based on well-understood techniques (no need to invent new language constructs)
Strong type system
Support for good software engineering practices

## Slide 61: P414 dataplane model
Control-plane

## Slide 62: P414 to P416 evolution
P4 v1.0
P416
core.p4
library.p4
arch.p4
small,
Standardized,
rarely change
Can be large,
manufacturer controlled,
frequent changes