## Slide 1: P4: specifying data planes http://P4.org
Mihai Budiu
VMware Research Group
VMware Techtalk March 30, 2017

## Slide 2: About Myself
Ph.D. from Carnegie Mellon
Researcher at Microsoft Research, Silicon Valley
  Distributed systems, security, compilers, cloud platforms, machine learning, visualization
Software engineer at Barefoot Networks
  Design and implementation of P4
Researcher at VMware Research Group
  Big data, P4

## Slide 3
P4 & Programmable networks
  Why should you care?
An introduction to P416
  P4 limitations
Conclusions
Presentation outline

## Slide 4: Networking 101
routers
Data packets

## Slide 5: Control and Data Planes
Control plane
Data plane
Interfaces
Switch architecture
packets

## Slide 6: Traditional switch architecture
Control plane
Data plane
Table management
Look-up tables (policies)
Switch ASIC
Control-plane CPU

## Slide 7: Software-Defined Networking
Dumb control plane
Data plane
Controller
Policies/signaling

## Slide 8: The P4 world
Programmable data plane
SW: P4
Dumb control plane
Upload program
Policies/signaling

## Slide 9: Not just for switches!
Programmable switches
FPGA switches
Programmable network cards
Software switches
Hypervisor switches
You name it…
Programmable data plane
SW: P4
Control plane

## Slide 10: How is this possible?
Hello
?
Datacenter
Most useful if you have your own network playground

## Slide 11: Data-planes
From now on in this presentation we only talk about the data-plane
We expect that SDN will continue to evolve the control-plane
Control plane
Data plane

## Slide 12: WHY SHOULD YOU CARE?

## Slide 13: Isn’t Open-Flow Enough?
Chart: Headers
| 1 | 1.1000000000000001 | 1.2 | 1.3 | 1.4
Headers | 12 | 15 | 36 | 40 | 41
Open-Flow version
Open-flow has never been enough: it keeps changing to describe new protocols

## Slide 14: has lots at stake
NSX is about programmable networks
  Flexibility in networking
  We are an industry leader
P4 will change the dynamics in the industry
  Device manufacturer ≠ device programmer
  Many network capabilities exposed to software

## Slide 15: Protocols = programs
VxLAN: 175 lines of P4
  Took 4 years from proposal to wide availability
NVGRE: 183 lines of P4
M. Shahbaz, S. Choi, B. Pfaff, C. Kim, N. Feamster, N. McKeown, J. Rexford, PISCES: A Programmable, Protocol-Independent Software Switch SIGCOMM 2016
40 times reduction in the size of the OvS parser
Much easier to add new protocols
Same performance

## Slide 16: Use only what you need
IETF has issued thousands of RFCs
Switch RAM and CPU is very expensive
Network operators can remove protocols
Simpler troubleshooting

## Slide 17: Network monitoring
measurements
(custom headers)
Monitoring
agent
In-Band Network Telemetry (INT)
Improving Network Monitoring and Management with Programmable Data Planes
By Mukesh Hira & LJ Wobker

## Slide 18: Optimize your network
Push application functionality in the network
High speed
Paxos Made Switch-y
Huynh Tu Dang, Marco Canini, Fernando Pedone, Robert Soulé
CCR April 2016

## Slide 19: Network = software
Use software engineering principles and tools
Upgrade your network at any time
Protocols = intellectual property

## Slide 20: P4.org Consortium
Carriers, cloud operators, chip co.s, networking, systems, universities,
start-ups

## Slide 21: AN INTRODUCTION to P416

## Slide 22: Language evolution
P4: Programming Protocol-Independent Packet Processors
Pat Bosshart, Dan Daly, Glen Gibb, Martin Izzard, Nick McKeown, Jennifer Rexford, Cole Schlesinger, Dan Talayco, Amin Vahdat, George Varghese, David Walker ACM SIGCOMM Computer Communications Review (CCR). Volume 44, Issue #3 (July 2014)
P4 v1.0 spec, reference implementation and tools released in Spring 2015 (mostly by Barefoot Networks), Apache 2 license, http://github.com/p4lang.
P416 spec, reference implementation and tools released in December 2016.

## Slide 23: P4 Community
http://github.com/p4lang
http://p4.org
Mailing lists
Workshops
P4 developer days
Academic papers (SIGCOMM, SOSR)

## Slide 24: Available Software Tools
Compilers for various back-ends
  Netronome chip, Barefoot chip, eBPF, Xilinx FPGA
  (open-source and proprietary)
Multiple control-plane implementations
  SAI, OpenFlow
Simulators
Testing tools
Sample P4 programs
Tutorials

## Slide 25: P416
Most recent revision of P4
Similar to C; strongly typed
Currently in draft form
Spec: http://p4.org/wp-content/uploads/2016/12/P4_16-prerelease-Dec_16.pdf
Reference compiler implementation (Apache 2 license): http://github.com/p4lang/p4c

## Slide 26: P416 data plane model
Data plane
P4
P4
P4
Programmable blocks
Fixed function

## Slide 27: Example packet processing pipeline
Programmable
parser
Packet (byte[])
Headers
eth
vlan
ipv4
Programmable
match-action
units
Metadata
eth
mtag
ipv4
Programmable
reassembly
Packet
Payload
err
bcast
port
Queueing/
switching
eth
mtag
ipv4
Headers

## Slide 28: Language elements
Programmable
parser
Programmable
match-action
units
Programmable
reassembly
State-machine; bitfield extraction
Table lookup; bitfield manipulation; control flow
Bitfield reassembly
Data-types
Bitstrings, headers, structures, arrays
External libraries
Support for custom accelerators
Target
description
Interfaces of programmable blocks
user
target

## Slide 29: Data Types
typedef bit<32> IPv4Address;
header IPv4_h { bit<4> version; bit<4> ihl; bit<8> tos; bit<16> totalLen; bit<16> identification; bit<3> flags; bit<13> fragOffset; bit<8> ttl; bit<8> protocol; bit<16> hdrChecksum; IPv4Address srcAddr; IPv4Address dstAddr; }
// List of all recognized headers struct Parsed_packet { Ethernet_h ethernet; IPv4_h ip; }
header = struct + valid bit
Other types: array of headers,
error, boolean, enum

## Slide 30: Parsing = State machines
parser Parser(packet_in b, out Parsed_packet p) { state start { b.extract(p.ethernet); transition select(p.ethernet.type) { 0x0800: parse_ipv4; default: reject; } }
state parse_ipv4 { b.extract(p.ip); transition accept; } }
src
IP header
dst
IP payload
type
ethernet header
start
parse_ipv4
reject
accept

## Slide 31: Actions
action Set_nhop(IPv4Address ipv4_dest, PortId port) { nextHop = ipv4_dest; outCtrl.outputPort = port; }
Action data; from control plane
~ Objects with a single method.
Straight-line code.
Reside in tables; invoked automatically on table match.
class Set_nhop {
IPv4Address ipv4_dest;
PortId port;
void run() {
nextHop = ipv4_dest; outCtrl.outputPort = port
}
}
Java/C++ equivalent code.

## Slide 32: Tables
dstAddr | action
0.0.0.0 | drop
10.0.0.1 | Set_nhop(10.4.3.4, 4)
224.0.0.2 | drop
192.168.1.100 | drop
10.0.1.10 | Set_nhop(10.4.2.1, 6)
table ipv4_match() { key = { headers.ip.dstAddr: exact; } actions = { Drop_action; Set_nhop; } default_action = Drop_action; }
Populated by the control plane
HashMap<K, Action>

## Slide 33: Match-Action Processing
Lookup table
headers &
metadata
Lookup
Lookup key
Action
action data
action code
Execute
Control plane
headers &
metadata
key
action
Code & data

## Slide 34: Control-Flow
control Pipe(inout Parsed_packet headers, in InControl inCtrl,// input port out OutControl outCtrl) { // output port IPv4Address nextHop; // local variable
action Drop_action() { … }
action Set_nhop(…) { … }
table ipv4_match() { … }
…
apply { // body of the pipeline ipv4_match.apply(); if (outCtrl.outputPort == DROP_PORT) return;
dmac.apply(nextHop); if (outCtrl.outputPort == DROP_PORT) return;
smac.apply(); } }
Ipv4_match
dmac
smac

## Slide 35: Packet Reassembly
control Deparser(in Parsed_packet p, packet_out b) { apply { b.emit(p.ethernet); b.emit(p.ip); } }
Convert headers back into a byte stream.
Only valid headers are emitted.

## Slide 36: P4 Program structure
#include <core.p4> // core library #include <target.p4> // target description
#include "library.p4" // library functions
#include "user.p4" // user program

## Slide 37: Architecture declaration
struct input_metadata { bit<12> inputPort; }
struct output_metadata { bit<12> outputPort; }
parser Parser<H>(packet_in b, out H headers);
control Pipeline<H>(inout H headers, in input_metadata input, out output_metadata output);
control Deparser<H>(in H headers, packet_out p);
package Switch<H>(Parser<H> p, Pipeline<H> p, Deparser<H> d);
Provided by the target manufacturer
H = user-specified header type
Parser
Pipeline
Deparser
Switch

## Slide 38: Support for custom “accelerators”
extern bit<32> random();
extern Checksum16 { void clear(); // prepare unit for computation void update<T>(in T data); // add data to checksum void remove<T>(in T data); // remove data from checksum bit<16> get(); // get the checksum for data added }
External function
External object with methods. Methods can be invoked like functions.
Some external objects can be accessed from the control-plane.

## Slide 39: Execution model
When a block is invoked (parser, control) it executes to completion on a separate thread
  All local variables are thread-local
  Only inter-thread communication possible through extern objects and functions
Execution triggered by outside event (e.g., packet arrival)
Actions execute atomically
  @atomic annotation for futher user-level control

## Slide 40: P4 software workflow
P4 program
P4 architecture
model
Data plane
P4 compiler
Tables
Dataplane runtime
Control-plane
target
User-supplied
API
Manufacturer supplied
control
signals
extern objects
API
LOAD
LOAD

## Slide 41: P4 LIMITATIONS

## Slide 42: Limitations of P416
The core P4 language is very small
  Highly portable among many targets
  But very limited in expressivity
Accelerators can provide additional functionality
  May not be portable between different targets
  Under construction: library of standard accelerators

## Slide 43: What is missing
Floating point
Pointers, references
Data structures, recursive data types
Dynamic memory management
Loops, iterators (except the parser state-machine)
Recursion
Threads
=> Constant work/byte of header

## Slide 44: What cannot be done in (pure) P4
Multicast or broadcast
Queueing, scheduling, multiplexing
Payload processing: e.g., encryption
Packet trailers
Persistent state across packets
Communication to control-plane
Inter-packet operations (fragmentation and reassembly)
Packet generation
Timers

## Slide 45: How are these done?
Multicast, broadcast, queueing, scheduling, multiplexing
  By target device, controlled by P4 metadata
Persistent state across packets (e.g. per-flow state)
  External objects: registers, counters, meters
Communication to control-plane
  External objects: learning providers
Packet generation
  Control-plane, or external objects
Reassembly, trailers:
  Not currently done

## Slide 46: P4 is not…
Active networking: a way for packets to inject new code
Programming the control plane: that is Software-Defined Networking
A tool for third parties to program the network
A language for:
  distributed computations
  network middleboxes (NFV)
  network operating systems

## Slide 47: Why use P4?
It is a language: you can specify the data-plane precisely
Expressive: express many packet-forwarding policies
High-level, type-safe: compiler-managed abstract resources
Software: treat network devices like software
Killer app: network monitoring

## Slide 48
Control plane
Data plane
UPLOAD
The P4 Programming- Language Interface
Creating a Programming Language Interface in a place where there wasn’t one.